Networking - IP Addresses

IP address

- 32 bits (IPv6 – 128 bits)

- host and network part

- static or dynamic

Subnet mask – number of bits used for network part of IP address

IP Address Classes

| Class | Use | Begins with | Left most octet | Number of Networks | Number of hosts on a network |
| --- | --- | --- | --- | --- | --- |
| A |  | 0 | 1 – 127 | 126 | 16,777,214 |
| B |  | 10 | 128 - 191 | 16,384 | 65,534 |
| C |  | 110 | 192 – 223 | 2,097,152 | 254 |
| D | Multicast | 1110 | 224 – 239 |  |  |
| E | Reserved | 1111 | 240 – 255 |  |  |

Private Address Space (three address ranges reserved by private network)

10.0.0.0 to 10.255.255.255 (10/8 prefix) 
172.16.0.0 to 172.31.255.255 (172.16/12 prefix) 
192.168.0.0 to 192.168.255.255 (192.168/16 prefix)

127.0.0.1 is reserved for the loopback address