Networking – Subnet Masks

The subnet mask works with the IP address.   For a subnet mask to be valid, its leftmost bits must be set to 1 and its rightmost bits must be set to 0.

The subnet mask is used to identify the subnet to which an IP address belongs.  It does this by performing a bitwise AND operation (returns true if both operands are true and false otherwise) on the subnet mask and IP address.

|  | Hosts | Netmask | Amount of a Class C |
| --- | --- | --- | --- |
| /30 | 4 | 255.255.255.252 | 1/64 |
| /29 | 8 | 255.255.255.248 | 1/32 |
| /28 | 16 | 255.255.255.240 | 1/16 |
| /27 | 32 | 255.255.255.224 | 1/8 |
| /26 | 64 | 255.255.255.192 | 1/4 |
| /24 | 256 | 255.255.255.0 | 1 |
| /23 | 512 | 255.255.254.0 | 2 |
| /22 | 1024 | 255.255.252.0 | 4 |
| /21 | 2048 | 255.255.248.0 | 8 |
| /20 | 4096 | 255.255.240.0 | 16 |
| /19 | 8192 | 255.255.224.0 | 32 |
| /18 | 16384 | 255.255.192.0 | 64 |
| /17 | 32768 | 255.255.128.0 | 128 |
| /16 | 65536 | 255.255.0.0 | 256 |