Tcpdump Man Page

TCPDUMP(1)                                             TCPDUMP(1)

NAME

tcpdump - dump traffic on a network

SYNOPSIS

tcpdump [ -adeflnNOpqStvx ] [ -c count ] [ -F file ]

[ -i interface ] [ -r file ] [ -s snaplen ]

[ -T type ] [ -w file ] [ expression ]

DESCRIPTION

Tcpdump  prints  out  the  headers of packets on a network

interface that match the boolean expression.

Under SunOS with nit or bpf: To run tcpdump you must  have

read  access to /dev/nit or /dev/bpf*.  Under Solaris with

dlpi: You must have read  access  to  the  network  pseudo

device, e.g.  /dev/le.  Under HP-UX with dlpi: You must be

root or it must be installed setuid to root.   Under  IRIX

with  snoop:  You  must  be  root  or it must be installed

setuid to root.  Under Linux: You must be root or it  must

be  installed  setuid  to  root.  Under Ultrix and Digital

UNIX: Once the  super-user  has  enabled  promiscuous-mode

operation  using  pfconfig(8),  any  user may run tcpdump.

Under BSD: You must have read access to /dev/bpf*.

OPTIONS

-a     Attempt to convert network and broadcast  addresses

to names.

-c     Exit after receiving count packets.

-d     Dump  the  compiled packet-matching code in a human

readable form to standard output and stop.

-dd    Dump packet-matching code as a C program  fragment.

-ddd   Dump  packet-matching code as decimal numbers (pre-

ceded with a count).

-e     Print the link-level header on each dump line.

-f     Print  `foreign'  internet  addresses   numerically

rather  than  symbolically (this option is intended

to get around serious  brain  damage  in  Sun's  yp

server -- usually it hangs forever translating non-

local internet numbers).

-F     Use file as input for the  filter  expression.   An

additional  expression given on the command line is

ignored.

-i     Listen  on  interface.   If  unspecified,   tcpdump

searches  the  system interface list for the lowest

numbered, configured up interface (excluding  loop-

back).   Ties  are  broken by choosing the earliest

match.

-l     Make stdout line buffered.  Useful if you  want  to

see the data while capturing it.  E.g.,

``tcpdump  -l  |  tee  dat''  or  ``tcpdump  -l   >

dat  &  tail  -f  dat''.

-n     Don't convert addresses (i.e., host addresses, port

numbers, etc.) to names.

-N     Don't  print  domain  name  qualification  of  host

names.  E.g., if you give this  flag  then  tcpdump

will print ``nic'' instead of ``nic.ddn.mil''.

-O     Do  not  run  the  packet-matching  code optimizer.

This is useful only if you suspect  a  bug  in  the

optimizer.

-p     Don't  put  the  interface  into  promiscuous mode.

Note that the interface  might  be  in  promiscuous

mode  for  some other reason; hence, `-p' cannot be

used as an abbreviation for `ether host  {local-hw-

addr} or ether broadcast'.

-q     Quick  (quiet?) output.  Print less protocol infor-

mation so output lines are shorter.

-r     Read packets from file (which was created with  the

-w  option).   Standard  input  is  used if file is

``-''.

-s     Snarf snaplen bytes of data from each packet rather

than the default of 68 (with SunOS's NIT, the mini-

mum is actually 96).  68 bytes is adequate for  IP,

ICMP,  TCP and UDP but may truncate protocol infor-

mation  from  name  server  and  NFS  packets  (see

below).   Packets  truncated  because  of a limited

snapshot  are  indicated   in   the   output   with

``[|proto]'', where proto is the name of the proto-

col level at which  the  truncation  has  occurred.

Note  that  taking  larger snapshots both increases

the amount of time it takes to process packets and,

effectively, decreases the amount of packet buffer-

ing.  This may  cause  packets  to  be  lost.   You

should  limit  snaplen  to the smallest number that

will capture the protocol information you're inter-

ested in.

-T     Force packets selected by "expression" to be inter-

preted the specified type.  Currently  known  types

are  rpc  (Remote  Procedure  Call), rtp (Real-Time

Applications protocol),  rtcp  (Real-Time  Applica-

tions  control  protocol), vat (Visual Audio Tool),

and wb (distributed White Board).

-S     Print absolute, rather than relative, TCP  sequence

numbers.

-t     Don't print a timestamp on each dump line.

-tt    Print an unformatted timestamp on each dump line.

-v     (Slightly  more)  verbose output.  For example, the

time to live and type of service information in  an

IP packet is printed.

-vv    Even  more verbose output.  For example, additional

fields are printed from NFS reply packets.

-w     Write the raw packets to file rather  than  parsing

and  printing  them out.  They can later be printed

with the -r option.  Standard  output  is  used  if

file is ``-''.

-x     Print  each packet (minus its link level header) in

hex.  The smaller of the entire packet  or  snaplen

bytes will be printed.

expression

selects  which  packets  will  be  dumped.   If  no

expression is given, all packets on the net will be

dumped.   Otherwise, only packets for which expres-

sion is `true' will be dumped.

The expression consists of one or more  primitives.

Primitives  usually  consist of an id (name or num-

ber) preceded by one or more qualifiers.  There are

three different kinds of qualifier:

type   qualifiers  say  what  kind  of thing the id

name or number refers  to.   Possible  types

are  host,  net and port.  E.g., `host foo',

`net 128.3', `port 20'.  If there is no type

qualifier, host is assumed.

dir    qualifiers  specify  a  particular  transfer

direction  to  and/or  from  id.    Possible

directions  are src, dst, src or dst and src

and dst.  E.g., `src foo', `dst net  128.3',

`src  or dst port ftp-data'.  If there is no

dir qualifier, src or dst is  assumed.   For

`null' link layers (i.e. point to point pro-

tocols such as slip) the  inbound  and  out-

bound  qualifiers  can  be used to specify a

desired direction.

proto  qualifiers restrict the match to a  particu-

lar  protocol.   Possible protos are: ether,

fddi,  ip,  arp,  rarp,  decnet,  lat,  sca,

moprc,  mopdl, iso, esis, isis, tcp and udp.

E.g., `ether src foo', `arp net 128.3', `tcp

port  21'.   If there is no proto qualifier,

all protocols consistent with the  type  are

assumed.   E.g., `src foo' means `(ip or arp

or rarp) src foo' (except the latter is  not

legal  syntax),  `net bar' means `(ip or arp

or rarp) net bar' and `port 53' means  `(tcp

or udp) port 53'.

[`fddi'  is  actually  an  alias  for  `ether'; the

parser treats them  identically  as  meaning  ``the

data  link  level  used  on  the  specified network

interface.''  FDDI  headers  contain  Ethernet-like

source and destination addresses, and often contain

Ethernet-like packet types, so you  can  filter  on

these FDDI fields just as with the analogous Ether-

net  fields.   FDDI  headers  also  contain   other

fields,  but  you  cannot name them explicitly in a

filter expression.]

In addition to the above, there  are  some  special

`primitive' keywords that don't follow the pattern:

gateway, broadcast, less,  greater  and  arithmetic

expressions.  All of these are described below.

More  complex  filter  expressions  are built up by

using the words and, or and not to  combine  primi-

tives.   E.g.,  `host  foo and not port ftp and not

port ftp-data'.  To save typing,  identical  quali-

fier lists can be omitted.  E.g., `tcp dst port ftp

or ftp-data or domain' is exactly the same as  `tcp

dst  port  ftp  or tcp dst port ftp-data or tcp dst

port domain'.

Allowable primitives are:

dst host host

True if the  IP  destination  field  of  the

packet  is  host,  which  may  be  either an

address or a name.

src host host

True if the IP source field of the packet is

host.

host host

True  if either the IP source or destination

of the packet is host.   Any  of  the  above

host  expressions  can be prepended with the

keywords, ip, arp, or rarp as in:

ip host host

which is equivalent to:

ether proto \ip and host host

If  host  is  a  name   with   multiple   IP

addresses,  each address will be checked for

a match.

ether dst ehost

True if the ethernet destination address  is

ehost.   Ehost  may  be  either  a name from

/etc/ethers or a number (see ethers(3N)  for

numeric format).

ether src ehost

True  if  the  ethernet  source  address  is

ehost.

ether host ehost

True if either the ethernet source or desti-

nation address is ehost.

gateway host

True  if  the packet used host as a gateway.

I.e., the  ethernet  source  or  destination

address  was  host but neither the IP source

nor the IP destination was host.  Host  must

be   a  name  and  must  be  found  in  both

/etc/hosts and /etc/ethers.  (An  equivalent

expression is

ether host ehost and not host host

which  can be used with either names or num-

bers for host / ehost.)

dst net net

True if the IP destination  address  of  the

packet  has a network number of net. Net may

be either a name  from  /etc/networks  or  a

network    number   (see   networks(4)   for

details).

src net net

True if the IP source address of the  packet

has a network number of net.

net net

True  if either the IP source or destination

address of the packet has a  network  number

of net.

net net mask mask

True  if the IP address matches net with the

specific netmask.  May be qualified with src

or dst.

net net/len

True if the IP address matches net a netmask

len bits wide.  May be qualified with src or

dst.

dst port port

True  if  the packet is ip/tcp or ip/udp and

has a destination port value of  port.   The

port  can  be  a  number  or  a name used in

/etc/services (see tcp(4P) and udp(4P)).  If

a  name  is  used,  both the port number and

protocol  are  checked.   If  a  number   or

ambiguous name is used, only the port number

is checked (e.g., dst port  513  will  print

both  tcp/login traffic and udp/who traffic,

and port domain will print  both  tcp/domain

and udp/domain traffic).

src port port

True  if  the packet has a source port value

of port.

port port

True if either  the  source  or  destination

port  of  the  packet  is  port.  Any of the

above port expressions can be prepended with

the keywords, tcp or udp, as in:

tcp src port port

which  matches only tcp packets whose source

port is port.

less length

True if the packet has a length less than or

equal to length.  This is equivalent to:

len <= length.

greater length

True if the packet has a length greater than

or equal to length.  This is equivalent to:

len >= length.

ip proto protocol

True if the packet  is  an  ip  packet  (see

ip(4P)) of protocol type protocol.  Protocol

can be a number or one of  the  names  icmp,

igrp,  udp, nd, or tcp.  Note that the iden-

tifiers tcp, udp, and icmp are also keywords

and must be escaped via backslash (\), which

is \\ in the C-shell.

ether broadcast

True if the packet is an ethernet  broadcast

packet.  The ether keyword is optional.

ip broadcast

True  if  the  packet  is  an  IP  broadcast

packet.  It checks for both  the  all-zeroes

and   all-ones  broadcast  conventions,  and

looks up the local subnet mask.

ether multicast

True if the packet is an ethernet  multicast

packet.   The  ether  keyword  is  optional.

This is shorthand for `ether[0] & 1 != 0'.

ip multicast

True  if  the  packet  is  an  IP  multicast

packet.

ether proto protocol

True  if  the packet is of ether type proto-

col.  Protocol can be a  number  or  a  name

like  ip,  arp, or rarp.  Note these identi-

fiers are also keywords and must be  escaped

via  backslash  (\).   [In  the case of FDDI

(e.g., `fddi protocol  arp'),  the  protocol

identification  comes from the 802.2 Logical

Link Control (LLC) header, which is  usually

layered  on top of the FDDI header.  Tcpdump

assumes,  when  filtering  on  the  protocol

identifier, that all FDDI packets include an

LLC header, and that the LLC  header  is  in

so-called SNAP format.]

decnet src host

True  if  the DECNET source address is host,

which  may  be  an  address  of   the   form

``10.123'',  or a DECNET host name.  [DECNET

host  name  support  is  only  available  on

Ultrix  systems  that  are configured to run

DECNET.]

decnet dst host

True if the DECNET  destination  address  is

host.

decnet host host

True if either the DECNET source or destina-

tion address is host.

ip, arp, rarp, decnet, iso

Abbreviations for:

ether proto p

where p is one of the above protocols.

lat, moprc, mopdl

Abbreviations for:

ether proto p

where p is one of the above protocols.  Note

that  tcpdump does not currently know how to

parse these protocols.

tcp, udp, icmp

Abbreviations for:

ip proto p

where p is one of the above protocols.

esis, isis

Abbreviations for:

iso proto p

where p is one of the above protocols.  Note

that tcpdump does an incomplete job of pars-

ing these protocols.

expr relop expr

True if the relation holds, where  relop  is

one  of  >, <, >=, <=, =, !=, and expr is an

arithmetic expression  composed  of  integer

constants  (expressed in standard C syntax),

the normal binary operators [+, -, *, /,  &,

|],  a  length  operator, and special packet

data accessors.  To access data  inside  the

packet, use the following syntax:

proto [ expr : size ]

Proto  is one of ether, fddi, ip, arp, rarp,

tcp, udp, or icmp, and indicates the  proto-

col layer for the index operation.  The byte

offset, relative to the  indicated  protocol

layer,  is  given by expr.  Size is optional

and indicates the number  of  bytes  in  the

field  of  interest;  it  can be either one,

two, or four,  and  defaults  to  one.   The

length  operator,  indicated  by the keyword

len, gives the length of the packet.

For example, `ether[0] & 1 != 0' catches all

multicast  traffic.  The expression `ip[0] &

0xf  !=  5'  catches  all  IP  packets  with

options.  The expression `ip[6:2] & 0x1fff =

0' catches only unfragmented  datagrams  and

frag  zero  of  fragmented  datagrams.  This

check is implicitly applied to the  tcp  and

udp  index operations.  For instance, tcp[0]

always means  the  first  byte  of  the  TCP

header, and never means the first byte of an

intervening fragment.

Primitives may be combined using:

A  parenthesized  group  of  primitives  and

operators  (parentheses  are  special to the

Shell and must be escaped).

Negation (`!' or `not').

Concatenation (`&&' or `and').

Alternation (`||' or `or').

Negation has highest precedence.   Alternation  and

concatenation  have  equal precedence and associate

left to right.  Note that explicit and tokens,  not

juxtaposition,  are now required for concatenation.

If an identifier is given without  a  keyword,  the

most recent keyword is assumed.  For example,

not host vs and ace

is short for

not host vs and host ace

which should not be confused with

not ( host vs or ace )

Expression  arguments  can  be passed to tcpdump as

either a single argument or as multiple  arguments,

whichever  is  more  convenient.  Generally, if the

expression contains  Shell  metacharacters,  it  is

easier  to  pass  it  as a single, quoted argument.

Multiple arguments  are  concatenated  with  spaces

before being parsed.

EXAMPLES

To  print  all  packets arriving at or departing from sun-

down:

tcpdump host sundown

To print traffic between helios and either hot or ace:

tcpdump host helios and \( hot or ace \)

To print all IP packets between ace and  any  host  except

helios:

tcpdump ip host ace and not helios

To  print  all  traffic  between  local hosts and hosts at

Berkeley:

tcpdump net ucb-ether

To print all ftp traffic through  internet  gateway  snup:

(note  that  the expression is quoted to prevent the shell

from (mis-)interpreting the parentheses):

tcpdump 'gateway snup and (port ftp or ftp-data)'

To print traffic neither sourced  from  nor  destined  for

local  hosts  (if you gateway to one other net, this stuff

should never make it onto your local net).

tcpdump ip and not net localnet

To print the start and end packets (the SYN and FIN  pack-

ets)  of  each  TCP conversation that involves a non-local

host.

tcpdump 'tcp[13] & 3 != 0 and not src and dst net localnet'

To print IP packets longer than  576  bytes  sent  through

gateway snup:

tcpdump 'gateway snup and ip[2:2] > 576'

To  print  IP broadcast or multicast packets that were not

sent via ethernet broadcast or multicast:

tcpdump 'ether[0] & 1 = 0 and ip[16] >= 224'

To  print   all   ICMP   packets   that   are   not   echo

requests/replies (i.e., not ping packets):

tcpdump 'icmp[0] != 8 and icmp[0] != 0'

OUTPUT FORMAT

The  output of tcpdump is protocol dependent.  The follow-

ing gives a brief description and examples of most of  the

formats.

Link Level Headers

If  the  '-e'  option  is  given, the link level header is

printed out.  On ethernets,  the  source  and  destination

addresses, protocol, and packet length are printed.

On FDDI networks, the  '-e' option causes tcpdump to print

the `frame control' field,   the  source  and  destination

addresses,  and  the  packet length.  (The `frame control'

field governs  the  interpretation  of  the  rest  of  the

packet.  Normal packets (such as those containing IP data-

grams) are `async' packets, with a priority value  between

0  and 7; for example, `async4'.  Such packets are assumed

to contain an 802.2 Logical Link Control (LLC) packet; the

LLC  header  is  printed if it is not an ISO datagram or a

so-called SNAP packet.

(N.B.: The following description assumes familiarity  with

the SLIP compression algorithm described in RFC-1144.)

On  SLIP  links, a direction indicator (``I'' for inbound,

``O'' for outbound), packet type, and compression informa-

tion  are  printed out.  The packet type is printed first.

The three types are ip, utcp, and ctcp.  No  further  link

information  is  printed for ip packets.  For TCP packets,

the connection identifier is printed following  the  type.

If the packet is compressed, its encoded header is printed

out.  The special cases are printed out as *S+n and *SA+n,

where  n  is  the  amount by which the sequence number (or

sequence number and ack) has changed.  If it is not a spe-

cial  case, zero or more changes are printed.  A change is

indicated by U (urgent pointer), W (window),  A  (ack),  S

(sequence  number), and I (packet ID), followed by a delta

(+n or -n), or a new value (=n).  Finally, the  amount  of

data  in  the  packet  and  compressed  header  length are

printed.

For example, the following line  shows  an  outbound  com-

pressed  TCP  packet,  with an implicit connection identi-

fier; the ack has changed by 6, the sequence number by 49,

and  the  packet  ID by 6; there are 3 bytes of data and 6

bytes of compressed header:

O ctcp * A+6 S+49 I+6 3 (6)

ARP/RARP Packets

Arp/rarp output shows the type of request  and  its  argu-

ments.   The  format  is  intended to be self explanatory.

Here is a short sample taken from the start of an `rlogin'

from host rtsg to host csam:

arp who-has csam tell rtsg

arp reply csam is-at CSAM

The  first  line  says that rtsg sent an arp packet asking

for the ethernet address  of  internet  host  csam.   Csam

replies with its ethernet address (in this example, ether-

net addresses are in caps and internet addresses in  lower

case).

This would look less redundant if we had done tcpdump -n:

arp who-has 128.3.254.6 tell 128.3.254.68

arp reply 128.3.254.6 is-at 02:07:01:00:01:c4

If  we had done tcpdump -e, the fact that the first packet

is broadcast and the second  is  point-to-point  would  be

visible:

RTSG Broadcast 0806  64: arp who-has csam tell rtsg

CSAM RTSG 0806  64: arp reply csam is-at CSAM

For the first packet this says the ethernet source address

is  RTSG,  the  destination  is  the  ethernet   broadcast

address,   the   type   field  contained  hex  0806  (type

ETHER_ARP) and the total length was 64 bytes.

TCP Packets

(N.B.:The following description assumes  familiarity  with

the  TCP  protocol  described  in RFC-793.  If you are not

familiar with the protocol, neither this  description  nor

tcpdump will be of much use to you.)

The general format of a tcp protocol line is:

src > dst: flags data-seqno ack window urgent options

Src  and  dst  are the source and destination IP addresses

and ports.  Flags are  some  combination  of  S  (SYN),  F

(FIN),  P  (PUSH)  or  R (RST) or a single `.' (no flags).

Data-seqno describes the portion of sequence space covered

by  the  data  in this packet (see example below).  Ack is

sequence number of the next data expected the other direc-

tion on this connection.  Window is the number of bytes of

receive buffer space available the other direction on this

connection.   Urg  indicates there is `urgent' data in the

packet.  Options are tcp options enclosed in angle  brack-

ets (e.g., <mss 1024>).

Src,  dst  and flags are always present.  The other fields

depend on the contents of the packet's tcp protocol header

and are output only if appropriate.

Here is the opening portion of an rlogin from host rtsg to

host csam.

rtsg.1023 > csam.login: S 768512:768512(0) win 4096 <mss 1024>

csam.login > rtsg.1023: S 947648:947648(0) ack 768513 win 4096 <mss 1024>

rtsg.1023 > csam.login: . ack 1 win 4096

rtsg.1023 > csam.login: P 1:2(1) ack 1 win 4096

csam.login > rtsg.1023: . ack 2 win 4096

rtsg.1023 > csam.login: P 2:21(19) ack 1 win 4096

csam.login > rtsg.1023: P 1:2(1) ack 21 win 4077

csam.login > rtsg.1023: P 2:3(1) ack 21 win 4077 urg 1

csam.login > rtsg.1023: P 3:4(1) ack 21 win 4077 urg 1

The first line says that tcp port  1023  on  rtsg  sent  a

packet  to  port  login on csam.  The S indicates that the

SYN flag was set.  The packet sequence number  was  768512

and    it   contained   no   data.    (The   notation   is

`first:last(nbytes)' which means `sequence  numbers  first

up to but not including last which is nbytes bytes of user

data'.)  There was  no  piggy-backed  ack,  the  available

receive window was 4096 bytes and there was a max-segment-

size option requesting an mss of 1024 bytes.

Csam replies with a similar packet except  it  includes  a

piggy-backed  ack  for  rtsg's SYN.  Rtsg then acks csam's

SYN.  The `.' means no flags were set.   The  packet  con-

tained  no data so there is no data sequence number.  Note

that the ack sequence number is a small integer (1).   The

first  time  tcpdump  sees a tcp `conversation', it prints

the sequence number from the packet.  On subsequent  pack-

ets  of  the conversation, the difference between the cur-

rent packet's sequence number and  this  initial  sequence

number is printed.  This means that sequence numbers after

the first can be interpreted as relative byte positions in

the  conversation's  data stream (with the first data byte

each direction being `1').  `-S' will override  this  fea-

ture,  causing the original sequence numbers to be output.

On the 6th line, rtsg sends csam 19 bytes of data (bytes 2

through  20 in the rtsg -> csam side of the conversation).

The PUSH flag is set in the packet.  On the 7th line, csam

says it's received data sent by rtsg up to but not includ-

ing byte 21.  Most of this data is apparently  sitting  in

the  socket  buffer since csam's receive window has gotten

19 bytes smaller.  Csam also sends one  byte  of  data  to

rtsg in this packet.  On the 8th and 9th lines, csam sends

two bytes of urgent, pushed data to rtsg.

If the snapshot was small enough that tcpdump didn't  cap-

ture  the  full  TCP  header, it interprets as much of the

header as it can and then reports ``[|tcp]''  to  indicate

the  remainder  could  not  be interpreted.  If the header

contains a bogus option (one with a length  that's  either

too  small  or  beyond  the  end  of  the header), tcpdump

reports it as ``[bad opt]'' and  does  not  interpret  any

further  options (since it's impossible to tell where they

start).  If the header length indicates options  are  pre-

sent but the IP datagram length is not long enough for the

options to actually be there, tcpdump reports it as ``[bad

hdr length]''.

UDP Packets

UDP format is illustrated by this rwho packet:

actinide.who > broadcast.who: udp 84

This  says that port who on host actinide sent a udp data-

gram to port who on host broadcast, the Internet broadcast

address.  The packet contained 84 bytes of user data.

Some  UDP services are recognized (from the source or des-

tination port number) and the higher level protocol infor-

mation   printed.   In  particular,  Domain  Name  service

requests (RFC-1034/1035) and Sun RPC calls  (RFC-1050)  to

NFS.

UDP Name Server Requests

(N.B.:The  following  description assumes familiarity with

the Domain Service protocol described in RFC-1035.  If you

are not familiar with the protocol, the following descrip-

tion will appear to be written in greek.)

Name server requests are formatted as

src > dst: id op? flags qtype qclass name (len)

h2opolo.1538 > helios.domain: 3+ A? ucbvax.berkeley.edu. (37)

Host h2opolo asked the domain  server  on  helios  for  an

address  record  (qtype=A)  associated  with the name ucb-

vax.berkeley.edu.  The query id was `3'.   The  `+'  indi-

cates  the  recursion  desired  flag  was  set.  The query

length was 37 bytes, not including the UDP and IP protocol

headers.   The  query operation was the normal one, Query,

so the op field was omitted.  If the op had been  anything

else,  it  would have been printed between the `3' and the

`+'.  Similarly, the qclass was the normal one, C_IN,  and

omitted.  Any other qclass would have been printed immedi-

ately after the `A'.

A few anomalies are checked and may result in extra fields

enclosed  in  square  brackets:   If  a  query contains an

answer,  name  server  or  authority   section,   ancount,

nscount,  or  arcount  are  printed  as  `[na]', `[nn]' or

`[nau]' where n is the appropriate count.  If any  of  the

response  bits  are  set  (AA,  RA or rcode) or any of the

`must be zero' bits  are  set  in  bytes  two  and  three,

`[b2&3=x]'  is printed, where x is the hex value of header

bytes two and three.

UDP Name Server Responses

Name server responses are formatted as

src > dst:  id op rcode flags a/n/au type class data (len)

helios.domain > h2opolo.1538: 3 3/3/7 A 128.32.137.3 (273)

helios.domain > h2opolo.1537: 2 NXDomain* 0/1/0 (97)

In the first example, helios responds to query id  3  from

h2opolo with 3 answer records, 3 name server records and 7

authority records.  The first  answer  record  is  type  A

(address)  and  its data is internet address 128.32.137.3.

The total size of the response was  273  bytes,  excluding

UDP  and  IP  headers.   The  op (Query) and response code

(NoError) were omitted, as was the class (C_IN) of  the  A

record.

In  the  second example, helios responds to query 2 with a

response code of non-existent domain  (NXDomain)  with  no

answers,  one  name  server and no authority records.  The

`*' indicates that the authoritative answer bit  was  set.

Since  there  were no answers, no type, class or data were

printed.

Other flag characters that might appear are `-' (recursion

available,  RA,  not  set) and `|' (truncated message, TC,

set).  If the `question' section doesn't  contain  exactly

one entry, `[nq]' is printed.

Note  that  name  server requests and responses tend to be

large and the default snaplen of 68 bytes may not  capture

enough  of  the  packet  to  print.   Use  the  -s flag to

increase the snaplen if you need to seriously  investigate

name server traffic.  `-s 128' has worked well for me.

NFS Requests and Replies

Sun  NFS  (Network  File  System) requests and replies are

printed as:

src.xid > dst.nfs: len op args

src.nfs > dst.xid: reply stat len op results

sushi.6709 > wrl.nfs: 112 readlink fh 21,24/10.73165

wrl.nfs > sushi.6709: reply ok 40 readlink "../var"

sushi.201b > wrl.nfs:

144 lookup fh 9,74/4096.6878 "xcolors"

wrl.nfs > sushi.201b:

reply ok 128 lookup fh 9,74/4134.3150

In the first line, host sushi sends a transaction with  id

6709  to  wrl (note that the number following the src host

is a transaction id, not the source  port).   The  request

was  112  bytes,  excluding  the  UDP and IP headers.  The

operation was a readlink (read symbolic link) on file han-

dle (fh) 21,24/10.731657119.  (If one is lucky, as in this

case, the file handle can be interpreted as a  major,minor

device  number pair, followed by the inode number and gen-

eration number.)  Wrl replies `ok' with  the  contents  of

the link.

In  the  third  line,  sushi  asks  wrl to lookup the name

`xcolors' in directory file 9,74/4096.6878.  Note that the

data printed depends on the operation type.  The format is

intended to be self explanatory  if  read  in  conjunction

with an NFS protocol spec.

If  the -v (verbose) flag is given, additional information

is printed.  For example:

sushi.1372a > wrl.nfs:

148 read fh 21,11/12.195 8192 bytes @ 24576

wrl.nfs > sushi.1372a:

reply ok 1472 read REG 100664 ids 417/0 sz 29388

(-v also prints the IP header TTL, ID,  and  fragmentation

fields,  which  have  been omitted from this example.)  In

the first line, sushi asks wrl to  read  8192  bytes  from

file  21,11/12.195,  at  byte  offset  24576.  Wrl replies

`ok'; the packet shown on the second  line  is  the  first

fragment  of  the reply, and hence is only 1472 bytes long

(the other bytes will follow in subsequent fragments,  but

these fragments do not have NFS or even UDP headers and so

might not be printed, depending on the  filter  expression

used).   Because  the  -v  flag is given, some of the file

attributes (which are returned in  addition  to  the  file

data)  are  printed:  the  file type (``REG'', for regular

file), the file mode (in octal), the uid and gid, and  the

file size.

If  the -v flag is given more than once, even more details

are printed.

Note that NFS requests are very  large  and  much  of  the

detail  won't be printed unless snaplen is increased.  Try

using `-s 192' to watch NFS traffic.

NFS reply packets do not explicitly identify the RPC oper-

ation.    Instead,   tcpdump  keeps  track  of  ``recent''

requests, and matches them to the replies using the trans-

action  ID.  If a reply does not closely follow the corre-

sponding request, it might not be parsable.

KIP Appletalk (DDP in UDP)

Appletalk DDP packets encapsulated in  UDP  datagrams  are

de-encapsulated  and  dumped as DDP packets (i.e., all the

UDP  header   information   is   discarded).    The   file

/etc/atalk.names  is  used  to translate appletalk net and

node numbers to names.  Lines in this file have the form

number    name

1.254          ether

16.1      icsd-net

1.254.110 ace

The first two lines give the names of appletalk  networks.

The third line gives the name of a particular host (a host

is distinguished from a net by the 3rd octet in the number

- a net number must have two octets and a host number must

have three octets.)  The number and name should  be  sepa-

rated    by    whitespace    (blanks    or   tabs).    The

/etc/atalk.names file may contain blank lines  or  comment

lines (lines starting with a `#').

Appletalk addresses are printed in the form

net.host.port

144.1.209.2 > icsd-net.112.220

office.2 > icsd-net.112.220

jssmag.149.235 > icsd-net.2

(If  the /etc/atalk.names doesn't exist or doesn't contain

an entry for some appletalk host/net number, addresses are

printed  in numeric form.)  In the first example, NBP (DDP

port 2) on net 144.1 node 209 is sending  to  whatever  is

listening  on  port  220 of net icsd node 112.  The second

line is the same except the full name of the  source  node

is  known  (`office').  The third line is a send from port

235 on net jssmag node 149 to broadcast  on  the  icsd-net

NBP  port  (note that the broadcast address (255) is indi-

cated by a net name with no host number - for this  reason

it's a good idea to keep node names and net names distinct

in /etc/atalk.names).

NBP (name binding protocol) and ATP (Appletalk transaction

protocol)  packets have their contents interpreted.  Other

protocols just dump the protocol name  (or  number  if  no

name is registered for the protocol) and packet size.

NBP packets are formatted like the following examples:

icsd-net.112.220 > jssmag.2: nbp-lkup 190: "=:LaserWriter@*"

jssmag.209.2 > icsd-net.112.220: nbp-reply 190: "RM1140:LaserWriter@*" 250

techpit.2 > icsd-net.112.220: nbp-reply 190: "techpit:LaserWriter@*" 186

The  first  line is a name lookup request for laserwriters

sent by net icsd host 112 and  broadcast  on  net  jssmag.

The nbp id for the lookup is 190.  The second line shows a

reply for this request (note that it has the same id) from

host  jssmag.209 saying that it has a laserwriter resource

named "RM1140" registered on port 250.  The third line  is

another  reply to the same request saying host techpit has

laserwriter "techpit" registered on port 186.

ATP packet formatting is  demonstrated  by  the  following

example:

jssmag.209.165 > helios.132: atp-req  12266<0-7> 0xae030001

helios.132 > jssmag.209.165: atp-resp 12266:0 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:1 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:2 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:3 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:4 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:5 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:6 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp*12266:7 (512) 0xae040000

jssmag.209.165 > helios.132: atp-req  12266<3,5> 0xae030001

helios.132 > jssmag.209.165: atp-resp 12266:3 (512) 0xae040000

helios.132 > jssmag.209.165: atp-resp 12266:5 (512) 0xae040000

jssmag.209.165 > helios.132: atp-rel  12266<0-7> 0xae030001

jssmag.209.133 > helios.132: atp-req* 12267<0-7> 0xae030002

Jssmag.209 initiates transaction id 12266 with host helios

by requesting up to 8 packets (the `<0-7>').  The hex num-

ber  at the end of the line is the value of the `userdata'

field in the request.

Helios responds with 8  512-byte  packets.   The  `:digit'

following  the  transaction  id  gives the packet sequence

number in the transaction and the number in parens is  the

amount  of  data  in the packet, excluding the atp header.

The `*' on packet 7 indicates that the EOM bit was set.

Jssmag.209 then requests that packets 3 & 5 be retransmit-

ted.   Helios  resends  them  then jssmag.209 releases the

transaction.   Finally,  jssmag.209  initiates  the   next

request.   The  `*'  on  the  request  indicates  that  XO

(`exactly once') was not set.

IP Fragmentation

Fragmented Internet datagrams are printed as

(frag id:size@offset+)

(frag id:size@offset)

(The first form indicates there are more  fragments.   The

second indicates this is the last fragment.)

Id  is  the  fragment  id.   Size is the fragment size (in

bytes) excluding the IP header.  Offset is this fragment's

offset (in bytes) in the original datagram.

The fragment information is output for each fragment.  The

first fragment contains the higher level  protocol  header

and  the  frag  info  is  printed after the protocol info.

Fragments after the first contain no higher level protocol

header  and  the frag info is printed after the source and

destination addresses.  For example, here is  part  of  an

ftp from arizona.edu to lbl-rtsg.arpa over a CSNET connec-

tion that doesn't appear to handle 576 byte datagrams:

arizona.ftp-data > rtsg.1170: . 1024:1332(308) ack 1 win 4096 (frag 595a:328@0+)

arizona > rtsg: (frag 595a:204@328)

rtsg.1170 > arizona.ftp-data: . ack 1536 win 2560

There are  a  couple  of  things  to  note  here:   First,

addresses  in  the  2nd  line  don't include port numbers.

This is because the TCP protocol information is all in the

first  fragment  and  we  have  no  idea  what the port or

sequence numbers are when we print  the  later  fragments.

Second,  the tcp sequence information in the first line is

printed as if there were 308 bytes of user data  when,  in

fact,  there  are 512 bytes (308 in the first frag and 204

in the second).  If you  are  looking  for  holes  in  the

sequence  space  or  trying to match up acks with packets,

this can fool you.

A packet with the IP don't fragment flag is marked with  a

trailing (DF).

Timestamps

By  default, all output lines are preceded by a timestamp.

The timestamp is the current clock time in the form

hh:mm:ss.frac

and is as accurate as the kernel's clock.   The  timestamp

reflects  the  time  the  kernel first saw the packet.  No

attempt is made to account for the time lag  between  when

the  ethernet  interface  removed the packet from the wire

and when the kernel serviced the `new packet' interrupt.

SEE ALSO

bpf(4), pcap(3)

AUTHORS

Van Jacobson, Craig Leres and Steven McCanne, all  of  the

Lawrence Berkeley National Laboratory, University of Cali-

fornia, Berkeley, CA.

The current version is available via anonymous ftp:

ftp://ftp.ee.lbl.gov/tcpdump.tar.Z

BUGS

Please send bug reports to tcpdump@ee.lbl.gov.

NIT doesn't let you watch your own outbound  traffic,  BPF

will.  We recommend that you use the latter.

Some attempt should be made to reassemble IP fragments or,

at least to compute the right length for the higher  level

protocol.

Name  server inverse queries are not dumped correctly: The

(empty) question section is printed rather than real query

in  the answer section.  Some believe that inverse queries

are themselves a bug and prefer to fix the program  gener-

ating them rather than tcpdump.

Apple  Ethertalk  DDP packets could be dumped as easily as

KIP DDP packets but aren't.  Even if we were  inclined  to

do  anything  to promote the use of Ethertalk (we aren't),

LBL doesn't allow Ethertalk on any of its networks so we'd

would have no way of testing this code.

A packet trace that crosses a daylight savings time change

will give skewed time stamps (the time change is ignored).

Filters  expressions  that  manipulate FDDI headers assume

that all FDDI packets are encapsulated  Ethernet  packets.

This  is true for IP, ARP, and DECNET Phase IV, but is not

true for protocols such as ISO CLNS.  Therefore, the  fil-

ter  may  inadvertently accept certain packets that do not

properly match the filter expression.