Lab 2 - Traffic Monitoring using ethereal

The ping command

- On the client machine, issue the ping command to the IP address of the client machine (have the command issue 5 pings).

- On the client machine, issue the ping command to the loopback interface (have the command issue 5 pings).

- Save the output of both ping commands to a file(s).

- Include the output of the commands in your lab report.

- Explain the difference between pinging the local Ethernet interface and the loopback interface.   This is a conceptual question on the role of the loopback interface; the answer will not be found in the response to the ping command.

The ping command

- From the client machine, ping the switch and record or save the results

- From the switch, ping the client machine and record the results

- From the server, ping the switch and record the results

- From the switch, ping the server machine and record results

- From the client machine, ping the server machine and record or save the results

- From the server machine, ping the client machine and record or save the results

- If any of these are unsuccessful, troubleshoot the problem; all 4 pings should be successful

Running ethereal

- Start ethereal

- Start a capture to capture packets on the network interface connected to the client.

- Ping the client machine.

- Stop the packet capture.

- Save the results of the captured traffic as a plain text file.   This is done by selecting Print in the File menu.   Save the details of the captured traffic, using the “print detail” option in the Print window.

- Start ethereal

- Start a capture to capture packets on the network interface connected to the client.

- Ping the server machine.

- Stop the packet capture.

- Save the results of the captured traffic as a plain text file.   This is done by selecting Print in the File menu.   Save the details of the captured traffic, using the “print detail” option in the Print window.